Chinese 12ch A/C
DMX Universe 2, Address 001
Switches On: 1, Off: 2-10

DMX Universe 2, Address 013
Switches On: 1, 3, 4, Off: 2, 5-10

Chinese 27 DC
DMX Universe 2, Address 049
Switches On: 1, 5, 6, Off: 2-4, 7-10

CTB24D 12ch DC
DMX Universe 2, Address 025
Switches On: 5, 6, 9, Off 1-4, 7, 8
LED Blinking (Twice per second) NOT receiving data!
LED Solid, Receiving valid LOR or DMX data

CTB16PC 16ch A/C Gen 3
Unit ID must be set using LOR Hardware Utility
LED Blinking (Twice per second) NOT receiving data!
LED Solid, Receiving valid LOR or DMX data
Black to Unit ID 3, DMX Universe 1 Address 49
Gray to Unit IDs 8 and 9, DMX Universe 2, Addresses 97 and 113
Metal to Unit IDs 7 and 8, DMX Universe 2, Addresses 81 and 97

LOR1602W Gen 1
DMX Universe 2, Address 049
Wheels to 0 and 4
LED Blinking (Twice per second) NOT receiving data!
LED Solid, Receiving valid LOR or DMX data

LOR1602W Gen 3
DMX Universe 1, Addresses 65 and 81
Use front panel to set addresses